## Slide 1
CAPSTONE 8
AI PCB Design Review Checklist Assistant
Project question: Can AI help beginners review simple PCB layouts, and what mistakes does it miss?
Three cases: 5 V regulator • LED indicator • 555 timer
Goal: combine AI suggestions with sources, ERC/DRC, calculations and human review
Note: sample findings are illustrative until actual board files and teacher feedback are added
CAPSTONE 8 • AI PCB REVIEW

## Slide 2
Method: AI is a first-pass assistant
A repeatable, evidence-led workflow
1. Collect schematic, PCB views, BOM, exact part numbers and design requirements
2. Apply the same source-grounded checklist to all three designs
3. Ask AI for Pass / Fail / Unknown, evidence, confidence and next verification step
4. Verify with datasheets, KiCad ERC/DRC, calculations and teacher review
5. Record false alarms, missed issues and unsupported claims
CAPSTONE 8 • AI PCB REVIEW

## Slide 3
Three example designs
What the checklist looks for
A — 5 V regulator: pinout, capacitors, current path, power dissipation and thermal limits
B — LED indicator: series resistor, LED polarity, resistor power and connector labels
C — 555 timer: exact pin mapping, local decoupling, timing network and output load
Evidence needed: actual schematic + board layout + exact manufacturer datasheets
CAPSTONE 8 • AI PCB REVIEW

## Slide 4
Verified checklist
Core review categories
Decoupling: capacitor close to supply pin; short, direct return path
Grounding: continuous, sensible return path; avoid bottlenecks; no universal split-plane rule
Trace width: justify from current, copper, layer, temperature rise and voltage drop
Footprints & mechanics: pad mapping, polarity, connector orientation, edge clearance
Final checks: ERC, DRC, thermal calculations, Gerbers, BOM and human sign-off
CAPSTONE 8 • AI PCB REVIEW

## Slide 5
What AI can get wrong
Error and miss analysis
Missed: hidden connectivity, wrong footprint pad numbers, thermal overload or narrow current paths
False alarm: a component is outside a cropped screenshot and AI calls it missing
Invented rule: “all boards must split analog and digital ground”
False confidence: “DRC clean means production-ready”
Control: require sources, mark unknowns, verify every high-priority finding
CAPSTONE 8 • AI PCB REVIEW

## Slide 6
Tool comparison & automation
Use a shared rubric, not impressions
ChatGPT: structured checklist and finding explanations
Gemini: independent second review on the same evidence
Perplexity: discover primary sources; open and verify them
KiCad ERC/DRC: deterministic checks against configured rules
Spreadsheet: dropdown status, automatic completeness score and unresolved-item tracking
CAPSTONE 8 • AI PCB REVIEW

## Slide 7
Conclusion & submission evidence
AI helps organize review; it does not certify a PCB
AI is most useful when constrained by a checklist and asked to show evidence
It cannot replace exact datasheets, netlist inspection, calculations or expert review
Add screenshots of each real board, both AI outputs, DRC/ERC reports and teacher comments
Sources: TI layout guidelines • Analog Devices grounding guidance • KiCad docs • Saturn PCB Toolkit
Final rule: unknown is not pass; unresolved high-risk findings block sign-off
CAPSTONE 8 • AI PCB REVIEW